## Slide 1
Improving Flash Flood Monitoring and Forecasting Capabilities in West Africa with Satellite Observations and Precipitation Forecasts
Humberto Vergara, Vanessa Robledo, Gonzalo Forero
December 11, 2023
Efthymios Nikolopoulos, Abigail Jones, Ankita Kukrety, Rutgers
Georgios Anagnostopoulos, Akshay Aravamudan, Xi Zhang, FIT
Viviana Maggioni, Malihe Nasibi, GMU
Jonathan J. Gourley, NOAA NSSL
Abdou Ali, AGRHYMET

## Slide 2: The team
Project: Machine learning based flash flood forecasting in West Africa with satellite observations
Machine Learning
Hydrologic Modeling
Satellite Hydrometeorology
Flash Flood Warning
Lead PI

## Slide 3: Flash flood warnings require high-resolution/low latency information
Hydrologic Response
Driving Precipitation
FF Likely
FF Very Likely
Desperate search for survivors after flash flood/landslide event in Mocoa, Colombia: 250 fatalities/100s injured Source: (BBC World, 2017)
IMERG Early: Near-Real Time Capabilities
Rainfall-driven short fused hazard
High rainfall rates
Rapidly evolving/Small spatial scales
~ 4 hours latency
Peak of Event
IMERG-based 4h Behind
Response from IMERG-based 4h Behind
Most recent IMERG
Present (Analysis)
Monitoring Challenge: Latency
Forecasting Challenge: Predictability

## Slide 4: A ML-based Flash Flood Forecasting System for West Africa
Monitoring Challenge: Short-term QPFs based on satellite inputs
Forecasting Challenge: Coupling with regional NWP
Development of a SERVICE for West Africa
Improving capabilities: Integration into existing operational system (WA partners)
Operational Hydrologic Modeling Tool

## Slide 5: Distributed hydrological modeling for flash flood prediction
PRECIPITATION
INFILTRATION
STORAGE CHANGE
RUNOFF
ROUTING
ROUTING
EVAPOTRANSPIRATION
INTERFLOW
EF5 models the macro-processes of the water cycle
Flamig, Z.L., Vergara, H. and Gourley, J.J., 2020. The Ensemble Framework For Flash Flood Forecasting (EF5) v1.2: Description and Case Study. Geoscientific Model Development Discussions, 13, 4943–4958, https://doi.org/10.5194/gmd-13-4943-2020, 2020.

## Slide 6: Distributed hydrological modeling for flash flood prediction
a-priori estimates of model parameters based on globally available geophysical data

## Slide 7: Côte d’Ivoire Flood June 2018: EF5 outputs
Unit Streamflow (m3 s-1 km-2)
Impacts: 18 reported fatalities and severe material damage
Sources reporting this event: Flash Flood Database, Flood List
Notes: EF5 simulation period: 2018-06-18 21:00 - 2018-06-19 21:00

## Slide 8: Establishing a robust baseline for short-term QPFs
https://pysteps.github.io
pySTEPS
Pulkkinen, S., D. Nerini, A. Perez Hortal, C. Velasco-Forero, U. Germann, A. Seed, and L. Foresti, 2019: Pysteps: an open-source Python library for probabilistic precipitation nowcasting (v1.0). Geosci. Model Dev., 12 (10), 4185–4219. doi:10.5194/gmd-12-4185-2019.

## Slide 9: Establishing a robust baseline for short-term QPFs
Lagrangian
Linda
Steps
Drainage Area = ~ 2 km2
FF Likely
FF Very Likely
IMERG with latency
‘Perfect’
Forecast
IMERG-based Simulation

## Slide 10: Establishing a robust baseline for short-term QPFs
Drainage Area = ~ 2 km2
FF Likely
FF Very Likely

## Slide 11: Understanding flash flood predictability in WA
Duration (hr) | 48
Distance (km) | 1,754.37
Mean velocity (km/hr) | 73.24
Mean area () | 227,897.63
Mean precipitation (mm/hr) | 7.39
Max precipitation (mm/hr) | 63.42
Duration (hr) | 48
Distance (km) | 1,754.37
Mean velocity (km/hr) | 73.24
 | 227,897.63
Mean precipitation (mm/hr) | 7.39
Max precipitation (mm/hr) | 63.42
Ramírez-Cardona, A., Robledo, V., Rendón, A., Henao, J. J., Hernandez, K. S., Rios, S. G., Mejia, J. F. (2022). Algorithm for Tracking Convective Systems (ATRACKCS) (v.1.0), Zenodo, 10.5281/zenodo.7025989
https://github.com/alramirezca/ATRACKCS
Max. Precip. rates on current track
Individual storm objects
Estimated track from centroids
Studying rain storms events in the West Africa domain

## Slide 12: Summary and ongoing efforts
We seek to realize the potential of satellite-based systems to provide timely flash flood warnings
ML-based nowcasting and very high resolution domain in Ghana
Capacity building for West Africa partners
Contact
Humberto Vergara – humberto-vergaraarrieta@uiowa.edu
Lab Website – https://ahwa.lab.uiowa.edu
SERVIR Project (Website coming soon!)
  Efthymios Nikolopoulos - efthymios.nikolopoulos@rutgers.edu